## Slide 1
BALL BALANCING
Students: Rawad Fakhreddine 6366
Aya Kreij 6497
Supervisor: Prof. Mohamad Aoude
Lebanese University
Faculty of Engineering III
Electrical and Electronic Department
Notes: Hello and welcome to our presentation on the Ball Balancing Platform Project using Computer Vision, Reinforcement Learning, and Arduino-controlled motors.
This innovative project was completed by Rawad Fakhreddine and Aya Kreij, under the supervision of Prof. Mohamad Aoude at the Lebanese University – Faculty of Engineering III.

## Slide 2
  Fine-tuned a YOLOv8 with a dataset to detect the tennis ball
  Use Computer Vision to detect and track the ball
  Compute the position, velocity, and acceleration of the ball
  Print the equipment and linkage using 3D Printing
  First try: Use a PID Controller to balance the ball
  Second try: Use Reinforcement Learning to train a model (agent)
  Calculate the linkage function to transform the tilt angle of the table to the necessary angle of rotation of each stepper motor
  Send Data from VS Code to Arduino via serial port
  Initialize the 2 stepper motors, and calculate the necessary steps using angle of rotation
TASKS OF THE PROJECT
1
Notes: The main goals of this project are:
To detect and track a tennis ball in real time using YOLOv8 and a webcam.
To calculate the ball’s position, velocity, and acceleration.
To train a Reinforcement Learning agent that can learn to stabilize the ball on the platform.
And finally, to control stepper motors using Arduino and a custom mechanical linkage system to tilt the platform

## Slide 3
2
FINE-TUNED A YOLOV8
  You Only Look Once Object detection algorithm that can find and identify objects
  YOLOv8 is for general-purpose datasets, we fine-tune it to detect the tennis ball only by training it on a custom dataset
  Different lighting conditions
  Varying positions and angles
  Having some clutter in the background
Notes: Computer Vision Module: A YOLOv8 model detects the ball’s location from webcam frames. These image coordinates are then converted into real-world positions using a pixel-to-centimeter conversion factor.

## Slide 4
COMPUTER VISION
  Detect and track the ball in real life using a webcam
  Computer captures frames
  Run YOLOv8 interference on the frame
  YOLOv8 outputs bounding boxes
  Calculating the center of the platform/table (red point)
  Calculating the center of the tennis ball by finding the 4 borders (blue point)
  These are the ball’s coordinates in the camera’s image frame (in pixels)
3
Notes: State Estimation: The ball’s velocity and acceleration are estimated by comparing positions over time. To reduce noise, we applied exponential smoothing and a deadband filter.

## Slide 5
4
Notes: Calculate the center of the ball by detecting it’s edge

## Slide 6
PRINT THE EQUIPMENT AND LINKAGE USING 3D PRINTING
  Design the equipment using SolidWorks
  Print it with a 3D Printing machine
  Print the linkage and the structure of the project
5
  Join all the linkages with the structure
  Used a Flexy with a 20cm width for the table
  Design a wooden stand for the camera
Notes: We Design the equipment using SolidWorks. Print the parts using a 3D printing.And finally, Join and construct the project

## Slide 7
6
  Y-axis
  X-axis
  (-,-)
  (+,+)
  (+,-)
  (-,+)
  Postion of the ball:
  Θx –
  Θy –
  Θx –
  Θy +
  Θx +
  Θy –
  Θx +
  Θy +
  The necessary rotation angle
Notes: This is a clear slide that show how the stepper motors should act in different cases of position of the ball

## Slide 8
FIRST TRY: PID CONTROLLER
7
  Compute the error = reference - position of the ball
  Uses the PID equation (for x & y): pid_x = (Kp * err_x) + (Ki * int_x) - (Kd * vel_mps[0])
  The output should be theta 4, which is the necessary tilt angle (x & y) of the table
  The PID is in a loop, where the errors are always updating due to feedback
Because we don’t have the transfer function so it’s very hard to solve this problem using a PID Controller!
Notes: We first attempted to control the ball using a PID controller. Although the PID worked under simple conditions, it failed in many edge cases due to the nonlinear nature of the system.

## Slide 9
SECOND TRY: USE REINFORCEMENT LEARNING
8
There are many versions of models. Each time, I am trying to improve the agent by giving more features and details, and trying to think of different cases. In the last version, I changed the training loop to increase difficulty gradually. The output is theta 4 (the necessary tilt table to balance the ball)
It gives a good result for the tilt angles of the table!
Notes: We then switched to Reinforcement Learning. The agent was trained in simulation and gradually introduced to harder starting conditions using curriculum learning. After training, the agent successfully learned how to keep the ball centered by producing smooth and adaptive tilt commands.

## Slide 10
REINFORCEMENT LEARNING AND AGENT
9
Ball_balance_env file:
This file defines the custom Gymnasium environment that simulates the dynamics of a ball on a tilting table. It provides the physical world in which the agent operates.
Simulates ball motion based on table tilt (θ4_x, θ4_y)
Computes observations: ball position and velocity
Provides rewards that penalize being far from the center or moving fast
Terminates episode if ball falls off the table or max steps are reached
Supports curriculum learning by adjusting the spawn difficulty.
Train_agent file:
This script creates and trains a reinforcement learning agent using the PPO algorithm from Stable-Baselines3. The agent interacts with the environment and learns how to balance the ball by tilting the table
Imports the custom environment
Trains the agent using model.learn(...)
Uses a curriculum strategy: trains progressively on 5 increasing difficulty levels
At each level, a new environment is created with greater initial ball displacement.
Saves the trained agent model for later use
Notes: The file Ball_balance_env defines the custom Gymnasium environment that simulates the dynamics of a ball on a tilting table. It provides the physical world in which the agent operates. The Train agent script creates and trains a reinforcement learning agent using the PPO algorithm from Stable-Baselines3. The agent interacts with the environment and learns how to balance the ball by tilting the table

## Slide 11
10
The Linkage Equation: It’s a nonlinear equation. comes from mechanism kinematics, particularly four-bar linkage theory, which is a classical topic in mechanical engineering. In our project, we use Brent's Method to solve it
Brent’s method is a root-finding algorithm that combines:
  Bisection method (safe, slow)
  Secant method (faster, no derivative)
  Inverse quadratic interpolation (even faster)
Linkage Function
Notes: The Linkage Equation: It’s a nonlinear equation. comes from mechanism kinematics, particularly four-bar linkage theory, we solve it using root_scalar

## Slide 12
#Format as string
data_str = f"X{theta2_x:.2f},Y{theta2_y:.2f}\n"
ser.write(data_str.encode()) # Send as bytes
time.sleep(0.05)
SERIAL PORT
11
TRANSFORM DATA FROM VS CODE TO ARDUINO:
// Capture serial data
void serialEvent() {
while (Serial.available()) {
char inChar = (char)Serial.read();
if (inChar == '\n') {
stringComplete = true;
} else {
inputString += inChar; }}}
VS CODE
ARDUINO IDE
Notes: Once the tilt angles are computed, they’re sent to the Arduino via serial communication.

## Slide 13
Arduino Circuit
12
Equipment:
  Arduino Uno
  2 stepper motors
  2 A4988 Drivers
  Connection leads
  Power supply
A stepper motor is a brushless DC electric motor that divides a full rotation into a number of equal steps, providing precise control over the motor's position and speed.
Notes: The Arduino parses the command, converts the angles into motor steps, and uses the AccelStepper library to smoothly move the motors.

## Slide 14
10
Put conditions for the stepper motor's rotation to keep the linkage safe
Transform the angle of rotation to steps, every 200 steps is a 360-degree rotation
The moveTo function can move the motor to the desired angle, where the position is absolute, the reference is (0,0)
Arduino Code
Notes: A full 360-degree rotation equals 200 steps — so we calculate the number of steps based on the desired angle and execute the motion accordingly.
To ensure safety, we added tilt limits and clamped angles to within ±25 degrees

## Slide 15
THIS WAS OUR BALL BALANCING PROJECT
THANK YOU
FOR WATCHING
Notes: This project demonstrates that Reinforcement Learning, when combined with vision-based control and Arduino motor actuation, can effectively stabilize a dynamic system like a ball-on-plate — entirely without classical modeling or manual tuning.
The trained agent was able to transfer from simulation to hardware, showing the power of data-driven control in physical systems.
We hope this project inspires others to explore intelligent control techniques in real-world robotics and automation.
Thank you for listening.